Enhanced IP
Dr. William Chimiak, Sam Patton, Stephen Janansky
[Speaker Notes: PURPOSE: INTRODUCE SOME NEW TECHNOLOGY. YOU’RE THE FIRST AUDIENCE WE’VE SHOWN THIS TO.]

---
What are we trying to do?
Experimental Solution for IPv4 Address Depletion
[Speaker Notes: OUR MAJOR GOAL IS TO OFFER SOLUTION FOR ADDRESS DEPLETION WE ALSO WILL SHOW HOW OUR PROTOCOL COULD ALSO BE USED AS AN IPV6 TRANSITION TECHNOLOGY.]

---
Introduction
- Introduction of a new protocol (Enhanced IP)
- Security Considerations
- Transition Requirements
- Proof of Concept Implementation
- Things that still need work

---
Enhanced IP

---
Enhanced IP
- 64-bit Enhanced IP
- 2.2.2.2.10.3.3.2
- All Enhanced IP addresses have a site address and a host address
- Site address: 2.2.2.2, is used to route packets over the public Internet to a router/NAT that is aware of Enhanced IP packet format.
- Host address: 10.3.3.2, used to route packets to a node behind the router/NAT that has the outside address of 2.2.2.2

---
Enhanced IP Network
EIP1
N1
N2
EIP2
2.2.2.1
2.2.2.2
10.3.3.254
10.1.1.254
10.3.3.2
10.1.1.2
Internet
Private Network 1
Private Network 2

---
Enhanced IP Network
EIP1
N1
N2
EIP2
2.2.2.1
2.2.2.2
10.3.3.254
10.1.1.254
10.3.3.2
10.1.1.2
Internet
Public Network 1
Public Network 2

---
Enhanced IP
Minimal changes at layer 2 and 3 of OSI to implement
  - does not replace ARP, routing protocols
- Uses IP Option 26 to extend the length of the IP header, 12 bytes per packet
- The NAT functionality used in Enhanced IP is stateless as opposed to the stateful nature of IPv4 NAT.
- Over time IP Option 26 MUST become part of fast path implementations.

---
N2
EIP2
10.3.3.2
EIP1
10.1.1.2
N1
2.2.2.1
2.2.2.2
Version
IHL
ToS
Total Length
Identification
Flag
Fragment Offset
Time to Live
Protocol
Header Checksum
10.1.1.2
2.2.2.2
0x9a
12
0
1
0
255.255.255.255
10.3.3.2
[Speaker Notes: Notice that the source address is presently 10.1.1.2 and the extended source address is set to -1 which is the IP address 255.255.255.255. Also notice the zero bit field for extended source address is set to zero. Remember how the 10.1.1.2 is in the IPv4 source field]

---
N2
EIP2
10.3.3.2
EIP1
10.1.1.2
N1
2.2.2.1
2.2.2.2
Version
IHL
ToS
Total Length
Identification
Flag
Fragment Offset
Time to Live
Protocol
Header Checksum
2.2.2.1
2.2.2.2
0x9a
12
1
1
0
10.1.1.2
10.3.3.2
[Speaker Notes: See how the source address 10.1.1.2 moves from the IPv4 source position to the enhanced IP source address. NOTICE HOW THE IPV4 SOURCE IS NOW 2.2.2.1 NOTICE HOW THE CHECKSUM CHANGED]

---
N1
N2
EIP1
EIP2
2.2.2.1
2.2.2.2
10.3.3.2
10.1.1.2
Version
IHL
ToS
Total Length
Identification
Flag
Fragment Offset
Time to Live
Protocol
Header Checksum
2.2.2.1
10.3.3.2
0x9a
12
1
0
0
10.1.1.2
0.0.0.0
[Speaker Notes: THE DESTINATION IP IS NOW 10.3.3.2. THE EXTENDED DESTINATION FIELD IS NO LONGER NEEDED SO IT IS SET TO ZERO.]

---
DNS: Using AAAA to lookup 64 bits
DNS
- EIP1 first sends an A record request for eip2.somesite.com and receives a failure back because there is no A record.
- EIP1 then sends a AAAA request for eip2.somesite.com and receives back 2001:0101:0202:0202:0a03:0302::0
EIP1
N1
N2
EIP2
10.1.1.2
10.1.1.254
2.2.2.1
2.2.2.2
10.3.3.254
10.3.3.2

---
DNS: Using AAAA to lookup 64 bits
DNS
2001:0101:0202:0202:0a03:0302::0 is really 2.2.2.2.10.3.3.2
EIP1
N1
N2
EIP2
10.1.1.2
10.1.1.254
2.2.2.1
2.2.2.2
10.3.3.254
10.3.3.2
[Speaker Notes: The 2001:0101 is an experimental IPv6 prefix we use. The next 8 bytes make up the enhanced ip address encoded in base 16 hex.]

---
Code
- Patches for Linux NAT
- Patches for OpenWRT
- Linux client/server
  - Runs ssh, samba, apache, firefox, etc, without modification or recompile of programs
- Versions of ping & traceroute that include IP options, netcat-like program

---
Security Considerations
- Similarly to IPv6, Enhanced IP means increased connectivity for IP addresses that were previously unreachable because of NATs.
- Firewall software is not presently aware of Enhanced IP addresses.
- Enhanced IP NAT devices must only forward packets to networks that are directly connected (e.g. 10.0.0.0/8)

---
Enhanced IP: Transition

---
Our Assumptions
- The core of the Internet is closer to being ready to pass packets with IP options en masse than it is for passing IPv6 packets en masse.
- Edge networks will allow the packets we’ll be introducing in this presentation if the economics of Enhanced IP makes sense to them.

---
What to do next?
- On Cisco
  - “ip options ignore”
- On Juniper
  - allow-ip-options 26
- Router not listed here:
  - Send command to sam@enhancedip.org
  http://www.enhancedip.org/docs/router-references

---
What to do next?
- Please pass IP option 26
- Email: sam@enhancedip.org
- Tweet: @EnhancedIP
- www.enhancedip.org

---
Questions?

---
Useful socket options
- setsockopt(fd, IPPROTO_IP, IP_OPTIONS, optdata, len);
- kernel equivalent is kernel_setsockopt()

---
At a high level
- glibc changes to getaddrinfo - 2001:0101 needs to return a struct sockaddr_ein. As opposed to a struct sockaddr_in6.
- connect() changes in the kernel to support a new struct sockaddr type
- 8 line change in existing NAT code to bypass inspection of Enhanced IP packets
- New NAT netfilter module to perform Enhanced IP address swapping and checksum update functions.
- Subtracts 12 bytes from TCP MSS to account for overhead of larger IP header caused by including the 12 bytes of options.